## Slide 1: Arduino 101
Val Manes
Department of Math & Computer Science

## Slide 2: Download Arduino Software
Link:
http://gencyber.ialab.dsu.edu/2016/Arduino/
Save it to your computer
Execute the file, accept all defaults

## Slide 3: Hardware
Microprocessor with hardware interfaces
  Digital I/O
  Analog I/O
  3.3v & 5v supply
Simple programming interface

## Slide 4: Arduino Uno

## Slide 5: Interfaces
Analog
  Read varying voltage, convert to number (0-1023)
  Light, temperature, distance
  Pins A0-A5
Digital
  Read on/off state or provide power on/off
  Pushbutton, LED, buzzer
  Pulse Width Modulation/PWM (pseudo-varying voltage)
  Pins D0-D13

## Slide 6: Arduino Integrated Development Environment
Tools to write, compile and execute sketches (programs)
Code is in C language (mostly)
Opening sketch provides default setup and loop functions

## Slide 7: Three sections to code
Global variables (constants)
  Before the void setup( )
  Define values used throughout program
void setup( )
  Initialization steps – set pin modes
  Executes once at start of program
  Set initial state of devices, if needed
void loop( )
  Main program execution
  Continually repeats

## Slide 8: Initial Sketch Code
void setup() {
// put your setup code here, to run once:
}
void loop() {
// put your main code here, to run repeatedly:
}

## Slide 9: C Statements
End with semicolon (except branching/loop statements)
Case sensitive
Curly braces { } mark blocks of code
  branches, loops, etc.

## Slide 10: Data Types
int – integer, whole number: 1 2 9999 -876
float – floating point, real number 1.234 -0.0003456
  double if you need greater precision than 7 digits
char – character, a single letter, digit, punctuation
  Enclosed in single quotes: ‘a’ ‘1’ ‘#’

## Slide 11: Variables
Names of memory spaces
Assign and modify values stored
Declare before use
  int total;
  float average;

## Slide 12: Sample Program – Blink LED
int led = 10;
void setup() {
pinMode( led, OUTPUT );
}
void loop() {
//turn LED on and off for off half second
digitalWrite( led, HIGH );
delay( 500 );
digitalWrite( led, LOW );
delay( 500 );
}

## Slide 13: Included Examples
C:\Program Files (x86)\Arduino\examples