## Slide 1: Welcome to Wifi

## Slide 2: This morning
You’ve gotten the grand tour
About us
Welcome, getting started, etc
How wireless works

## Slide 3: But first
Why talk about how wifi works?
Lets just do l337 hax

## Slide 4: On your honor…

## Slide 5: B4 the hax
We need to know how this stuff works

## Slide 6: Linux??

## Slide 7: A Tail of 2 Addresses
MAC Address:
  Like your name
  Given when made
IP Address
  Like your mailing address
  Might change from time to time

## Slide 8: How they’re different
MAC Addresses
  a8:96:8a:f1:ff:c6
  First part = manufacturer
“Can’t be changed”
  But it can be spoofed
Allows communication to your neighbor
  Like a router
Can’t talk outside your network
IP Addresses
  192.168.10.5
  Changes all the time
Lets you communicate outside your network

## Slide 9
Notes: How to find your mac address under windows. This screenshots shows the MAC address for the network and Bluetooth adapter circled in red.
The IP address for the network adapter is circled in yellow.

## Slide 10
Notes: The physical network and wireless network adapter’s mac addresses are circled in red. The IP address of the physical Ethernet adapter is circled in yellow.
The wireless adapter isn’t connected to any network, therefore there is no IP address.

## Slide 11: ARP
Connect:
  IP and MAC
Computer: What is 192.168.1.1’s MAC?
192.168.1.1: I’m a8:91:8a:b2:df:f6
Run: arp -a

## Slide 12: Wireless Spectrum
9-100 Khz- Aircraft, ship navigation
100Khz-1Mhz: AM Radio
Around 10 Mhz: Shortwave Radio
Around 100 Mhz: FM Radio
Between FM and 1Ghz: TV
1Ghz: Cell Phones
10 Ghz + WiMax and Satellite

## Slide 13: WiFi Goodness
We use radio waves to communicate- duh
Radios transmitting at 2.4 or 5Ghz
  Then we separate channels in-between
  Why these frequencies?
  Who is wifi’s biggest enemy?
Notes: They’re free frequencies, unlicensed. Initially intended to be used for non-communication purposes
What non-communicating device uses radio waves?

## Slide 14
Notes: These may also use the same frequency and interfere
How can we avoid this?

## Slide 15: Frequencies/Channels for 2.4 Ghz

## Slide 17
Notes: Also operate at around 2.4 Ghz
How does wifi work with these around? Usually it does, but if the microwave’s shielding may be weak it can interfere

## Slide 18: Let’s first talk about wireless cards:

## Slide 19: Transmit Power (TX)
How far a card can actually transmit
Usually expressed in milliwatts (mW)
Consumer cards usually are around 30mW (+14.8 dBm)
Professional gear is around 300 mW (+24.8 dBm)

## Slide 21: Sensitivity
Often overlooked in favor of TX
What good is it to transmit great distances but not receive a response?
Usually measured in dBM (decibels relative to 1 mW)
  The more negative the number, the better for receiving when looking at cards
  -90 is better than -86

## Slide 22: AP Sensitivity
When you’re looking at how many dBm your access point is, the closer to 0 the better
It’s backwards and a little confusing at first
Buying antenna: -dBm better
AP signal: close to 0 dBm better

## Slide 23: AP Sensitivity

## Slide 24: Sensitivity
Typical values are -80 dBm to -90 dBm
Each 3 dBm change represents doubling of sensitivity
  High end cards get as much as -93 to -97 dBm
Convert mW to dBm:

## Slide 25: Chipset
We won’t spend too much time on this
Essentially what “drives” the card and tells it how to operate
Some chipsets are more hacker friendly than others
  Ralink

## Slide 26: Antenna Types
Omnidirectional
  Extends your range in all directions
Directional
  Let’s you focus your signal in a particular direction
Sensitivity – measured in dBi
  dBi - gain of an antenna as referenced to an ISOTROPIC (omnidirectional) source
  Remember, every 3 dBi = double the sensitivity

## Slide 27: Omnidirectional

## Slide 29: Alfa AWUS051NH
500mW High Gain 802.11a/b/g/n
5dBi and 9dBi omnidirectional antennas
  One antenna is a little over double as sensitive (4dB)

## Slide 30: Outdoor Antennas

## Slide 31: Cantennas!
People have found ways to modify cans and other cylindrical objects to make homemade directional antennas
They actually work, and some are pretty amusing
http://support.jefatech.com/cantenna/

## Slide 32: Pringles Can?

## Slide 33: Pringles Cantenna

## Slide 36: IEEE802.11
We know: B, G, A, N, AC -> Right?
  B: Old and slow, 2.4 Ghz
  A: Not many use, 5Ghz!!
  G: Not as old or as slow as B, 2.4 Ghz
  N: Pretty good, fast, etc, 2.4 or 5 Ghz!
  AC: Real nice 5Ghz!!

## Slide 37: Watch wireless connect
Open Wireshark
Applications>Internet>Wireshark
Select wlan0, click Start

## Slide 38: And…. Nothing Happens…
Notes: Right now, your adapter is playing by the rules. Its only listening to the traffic that’s being sent to it… There is no traffic being sent to it, so there is nothing to display.

## Slide 39: Connect to a Network
Network Manager >
  Select your network

## Slide 40: Listening to yourself isn’t much fun

## Slide 41: airmon-ng
Enables monitoring of wireless interfaces
Forces your adapter into “monitor” mode
  Basically: creeper mode

## Slide 42
Notes: Running airmon-ng by itself will list all of the current wifi adapters and tell you if any monitors exist
Airmon-ng check kill will find all of the programs that are using the wireless adapter and kill them off

## Slide 43: Watch wireless connect
Open Wireshark
Applications>Internet>Wireshark
Select mon0, click Start

## Slide 44: Problem
Your Routers/APs spill all of their details...
  Broadcast TONS of info that we LOVE to have!
  BSSID: Basic service set identification
    Contains: SSID and MAC Address
      SSID: Service Set Identifier
      MAC: Your hardware address
  What if we hide this info??
Notes: You can’t hide it!!!
You can hide the SSID